## Slide 1: Multi-Cell RTT + AoA Positioning Demo
Location
06/24/2021
@qualcomm

## Slide 2: Field Test Network Setup
ISD
50m
50m
65m
90m
160m
127m
135m
gNBs
  ZTE 64 TxRUs with positioning capability
  30~40 meters above ground
  Tx Power: ???
  Down tilt:
    gNB 1(PCI 1), 10.3
    gNB 2(PCI 2), 7.9
    gNB3 (PCI 993), 18
    gNB4 (PCI 996), 21.5
    gNB5 (PCI 90),20.5
UE:
  SDX60 supporting up to 16 cells simultaneously for positioning
Location server:
  Designed and operated by QC
SA mode with 100 MHz @n41
gNB1
gNB2
gNB3
gNB4
gNB5

## Slide 3: Overview of Test Routes

## Slide 4: Outdoor Test Route
170m
100m
45m
30m
60m
115m
90m
110m
35m

## Slide 5: Indoor Test Route
150m
140m
130m
100m

## Slide 6: Reference Signal Configuration
PRS
  Periodicity： 160ms
  # of Slots： 1 slot
  # of symbols per slot： 2 symbol
  Comb： comb2
SRS for positioning
  Periodicity： 160ms
  Slots： 1 slot
  # of symbols per slot： 2 symbol
  Comb： comb4

## Slide 7: Network Architecture

## Slide 8: Call Flow
Proprietary messages

## Slide 9: MC-RTT Demo Video

## Slide 10
/ /
5G NR positioning joint field trial results
Based on round trip time (RTT) and angle of arrival (AoA)
Multi-cell RTT and AoA based implementation improves accuracy
Raw* positioning accuracy
Line-of-sight (LOS) condition trial route:
*Instantaneous location estimates with no temporal processing, no GNSS or other sensor data assistance
 | Horizontal Accuracy |  | Vertical Accuracy | 
 | 50th-percentile | 80th-percentile | 50th-percentile | 80th-percentile
Single-cell Positioning | 1.6 m | 2.1 m | 0.8 m | 1.2 m
Multi-cell Positioning | 0.6 m | 1.0 m | 0.5 m | 1.0 m

## Slide 11
/ /
5G NR positioning joint field trial results
Based on round trip time (RTT) and angle of arrival (AoA)
Wide-area outdoor 5G multi-cell positioning provides high accuracy even in challenging deep indoor conditions
Raw* positioning accuracy
Indoor trial route with outdoor network:
*Instantaneous location estimates with no temporal processing, no GNSS or other sensor data assistance
 | Horizontal Accuracy |  | Vertical Accuracy | 
 | 50th-percentile | 80th-percentile | 50th-percentile | 80th-percentile
Good coverage | 1.5 m | 2.3 m | 0.6 m | 1.2 m
Edge coverage | 5.0 m | 7.0 m | 1.1 m | 2.2 m

## Slide 12
/ /
5G NR positioning joint field trial results
Based on round trip time (RTT) and angle of arrival (AoA)
Wide-area outdoor 5G multi-cell positioning provides high accuracy even in challenging deep indoor conditions
Raw* positioning accuracy
Indoor trial route with outdoor network :
*Instantaneous location estimates with no temporal processing, no GNSS or other sensor data assistance
 | Horizontal Accuracy |  | Vertical Accuracy |  | 50th-percentile RSRP (dbm) | Number of Test Points
 | 50th-percentile | 80th-percentile | 50th-percentile | 80th-percentile |  | 
Test Route1 | 1 | 1.7 | 0.75 | 1.23 | -63 | 15
Test Route2 | 1.59 | 2.58 | 0.48 | 1.13 | -84 | 46
Test Route3 | 6.02 | 7.63 | 0.87 | 2.1 | -95 | 51
Test Route4 | 4.31 | 5.23 | 1.54 | 2.07 | -92 | 33

## Slide 14
/ /
5G NR positioning joint field trial results
Based on round trip time (RTT) and angle of arrival (AoA)