## Slide 1
Comments on ICV ADS general technical requirements
Item | Comments
 | According to GB/T 34590, there is no such a definition called “safety policy”, so it shall change to “Safety measure” and in Chinese version the terms should change from “安全策略” to “安全措施”
 | Not clear about the definition of 30s, is it: a) AD system check driver ability in every 30s was enough, or b) feature shall check driver ability in all last 30s – which means ADS always check it. From chapter 6.1.3.2, the definition was likely to be item a). Combine the timescale in chapter 6.2.4.2, 30s might be a very relax requirement.
 | 10s is a little bit long since introduce higher requirement on available road model distance from perception/HDMAP. Check if can be changed to 5s.
 | In critical scenarios, MRM might not be able to lead the vehicle to complete stop, suggest to add a maximum MRM duration time to avoid AD system stuck in MRM.
 | Item b) Chinese version and English version are not the same. And driver might be mode confusion if AD system seamless transfer to driving assistance functions such as LKS even though their HMI are different. Suggest to enter manual driving once AD system deactivated.
 | Item b) suggest that ADS directly exit if driver intervenes exceed curtain threshold, avoid combination between manual driving and AD system in one vehicle platform (e.g., long. control in manual driving while lat. control in AD mode) Item c) it was hard to determine whether driver focus on DDT or not, and we can find same words in several items but no clear definition about it, so just leave the space for ADS manufacturer?