## Slide 1: SecType3 with smaller SCS - PRB range issue
Date 14-09-2022

## Slide 2: Problem Statement
O-RAN YANG files and the M-plane spec is ambiguous when it comes to the definition of PRBs that can be supported in an endpoint.
ORAN has the following two parameters to limit the number of PRBs in an endpoint
Parameter: // One value for all the numerologies leaf max-prb-per-symbol { type uint16; description "Max number of prbs within one symbol that can be processed by endpoint or processed collectively by group of endpoints sharing capacity"; } | Parameter: // Per numerology leaf number-of-prb { type uint16; mandatory true; description "Determines max number of PRBs that will be used in all sections per one symbol. This is affecting allocation of resources to endpoint. Value shall not exceed constraint defined by max-prb-per-symbol of endpoint type. In addition, sum (over all used endpoints within a group of endpoints sharing resources) of number-of-prb rounded up to the nearest value from prb-capacity-allocation-granularity shall not exceed max-prb-per-symbol of the group."; }
This possibly means the max addressable PRBs. For sectionType=1, it is fair to assume that O-DU can only address the number-of-prb consecutive PRBs starting from offset-to-absolute-frequency-center. But what about SectionType=3 endpoints where offset-to-absolute-frequency-center is not valid? This is the issue to be addressed. Issue (not related to this proposal): This is problematic for mixed-numerology enabled endpoints with different values for different numerologies. | This possibly means the max that can be used.

## Slide 3: Problem Statement
100 MHz NR FR1 carrier with SCS 15 kHz (546 RB), SCS 30 kHz (273 RB)
An example problematic use case is to have two 15 kHz SSBs in close to the two ends of the frequency grid as below but have an O-RU that can only address 273 PRBs per endpoint
Such O-RU potentially needs two eAxCs to be able to address this example.
However, if SectionType=3 endpoints are used, the beginning of grid is not known by M-plane and O-RU does not know where the start of the grid is to start counting max-prb-per-symbol.
Example scenario

## Slide 4: Solution #1
To change the definition of offset-to-absolute-frequency-center as below
  Description
    "This provides value of freqOffset to be used if section type 3 is not used in case of section type 1 and the minimum possible value for freqOffset in case of section type 3. See freqOffset in CUS-plane. offset-to-absolute-frequency-center defines the relative spacing between the centre of RE#0 of RB#0 to the center-of-channel-bandwidth. If offset-to-absolute-frequency-center for NR with SCS=15kHz is odd, it implies that 7.5kHz shift as indicated by the 3GPP parameter frequencyShift7p5khz for UL is applied, which means enable the NR UL transmission with a 7.5 kHz shift to the LTE raster, as defined in 3GPP TS 38.331. When type (in tx/rx-array-carrier) is DSS, 'offset-to-absolute-frequency-center' indicates the 1st RE of 1st RB of NR.";

## Slide 5: Solution #2
To set a reference point for sectionType=3 endpoints to mark the start of the grid, we need a new (optional) parameter with a backward compatible default value as below
  Name
    min-allowed-freqoffset-secttype3
      Or
    offset-to-absolute-frequency-center-st3
  Definition
    This parameters defines the spacing between the centre of the lowest subcarrier that can be addressed in the endpoint and the center-of-channel-bandwidth in steps of one half the subcarrier spacing.
  Default value
    The default value points to the center of the lowest subcarrier in the BW.
We should change the definition of max-prb-per-symbol as
  Max number of prbs within one symbol that are addressable and can be processed by endpoint or processed collectively by group of endpoints sharing capacity. The lowest subcarrier that can be addressed (reference start for this parameter) is defined by offset-to-absolute-frequency-center for section type 1 endpoints and by min-allowed-freqoffset-secttype3 (/offset-to-absolute-frequency-center-st3) for section type 3 ones.
  This may still be problematic for mixed-numerology enabled eAxCs with different values for different numerologies. But that issue exists whether we include the changes or not.