## Slide 1: V2X 技术现状与SOTIF相关思考

## Slide 2: 目录
C-V2X 技术特点
C-V2X 技术现状及趋势
V2X SOTIF 相关用例及思考

## Slide 3: 为未来 自动驾驶汽车铺平道路
为汽车互联平台提供关键技术
能效优化处理
多源信息融合
自动驾驶汽车
车载智能
C-V2X统一连接
3D地图测绘
与精准定位

## Slide 4: C-V2X移动车联在多维度上拥有关键优势
C-V2X
更大通信范围
更高可靠性
支持高密度通信
支持高速通信
可再利用汽车行业DSRC/C-ITS高层协议
R-14
自我管理功能
可降低成本和复杂度
可同步远程信息处理平台
利用移动数据生态系统
向5G发展的强大潜能

## Slide 5: C-V2X 定义了两种互补的传输模式
1. PC5 operates on 5.9GHz; whereas, Uu operates on commercial cellular licensed spectrum 2. RSU stands for roadside unit.
Uu 接口
如：前方2公里有事故
V2N
(Uu)
V2N
(Uu)
  网络通信
  “Uu”接口上的V2N，
  运行于传统的移动宽带授权频段
eNodeB
PC5 接口
如：位置、速度等
V2V
(PC5)
V2P
(PC5/)
V2P
(PC5)
V2I
(PC5)
V2I
(PC5)
直接通信
V2V, V2I, 和 V2P on “PC5” 接口,
运行于ITS 频段 (比如 ITS 5.9 GHz)
独立于蜂窝网络
RSU
Notes: C-V2X will define two transmission modes that work together to enable a broad range of automotive use cases:
Direct communications – Enhancing LTE Direct device-to-device communications, by utilizing what is called the PC5 Interfacet o enable exchange of real-time information between vehicles traveling at fast speeds, in high-density traffic, and even out of mobile network coverage.
  Supports a mechanism where cars can broadcast messages (e.g., their location, speed) to other cars directly at 100s of meters range at 100msec duty cycle.
  The PC5 interface was first introduced in Release 12 3GPP when a D2D Discovery and communications system was first defined.
  Now in R14 we are enhancing this interface to deal with high Doppler, improve synchronization, latency etc.
  Works both in and out of network coverage.
  Suitable for V2V safety and other latency sensitive use cases
Network communications - Leveraging existing infrastructure and ubiquitous coverage of existing LTE networks (optimized LTE Broadcast and unicast) to bring additional services, such as, finding open parking space or alerting to an accident a few miles ahead.
  It utilizes the cellular network and the Uu Interface which is the interface you normally use to access the cellular network.
  In this mode the network can communicate with the cars using the cellular broadcast system (called eMBMS), while vehicles can communicate with the network via unicast over the regular WAN connection and the Uu interface.
  Suitable for more latency tolerant use cases

## Slide 6: C-V2X移动车联能降低基础设施部署成本
得益于蜂窝网络越发密集，路侧单元(RSU)将与4G/5G小单元结合部署
有Uu接口的4G/5G小单元
有直接链路或PC5接口的路侧单元

## Slide 7: 高精度定位是 实现V2X车联网的关键
      精准定位
      运用GNSS全球卫星系统和精准定位服务技术，实现小于一米的定位精度
      行驶方向
      通过GNSS全球卫星系统定位计算，直接获取行车方向信息。
      精确时间信息 使用GNSS全球卫星系统作为主要时间同步源。
      行驶速度
      通过GNSS全球卫星系统定位计算，直接获取准确行车速度信息。
时间
车速
位置
驶向
时间
车速
位置
驶向
GNSS

## Slide 8: 从多方面加强汽车定位性能
频繁 更新
保证非常频繁的更新，来提供更新、更准确的定位信息。（例如汽车至少每100ms，就给V2X车联网应用发送一次最近的位置信息。）
更加 精准
拥有专为V2X车联网和自动驾驶高度集成的半米级准确度（精度级别到如能识别不同车道）
随时 随地
结合精准GNSS全球卫星系统定位和传感器输入信息，来在任何地点提供准确的定位，包括密集城市环境，室内停车场和楼层间互通。

## Slide 9: 为V2X车联网和自动驾驶发展定位技术
无论何时何地，都要提供更精准的定位信息
行驶导航/紧急救援/远程监管
普通定位
V2X 车联网安全增强
精准定位 <2m
超高精度定位 <<1m
自动驾驶
需要发射更多卫星来加强准确度和使用性
Glonass
俄罗斯格洛纳斯卫星系统
BDS 中国北斗卫星系统
Galileo 伽利略卫星系统
QZSS 日本准天顶卫星系统
卫星增强系统(SBAS)
基于卫星的普通导航
GPS 美国全球定位系统
使用单轴传感器进行
2D 二维航迹推算(DR)
利用更好的传感器以将准确度和使用性拓展到更多地区
6DOF 6向自由度
MEMS微机电传感器
3D 三维航迹推算(3D DR)
更高频更新
更精准的定位技术
更高频率 => 10Hz
L1 校准服务
摄像头视频输入输出
自动驾驶时代
随时、随地均可超高精度定位
多频GNSS全球导航卫星系
RF射频和数字基带信号
软件服务
校准服务
5G NR技术V2X移动车联

## Slide 10: 车载智能: C-V2X与其它传感器技术相结合
ADAS
先进驾驶辅助系统
汽车大脑支持驾驶流程的自动化
整合计算能力
传感器融合 机器学习
道路规划
V2X无线传感器 穿透式、360◦非视距传感、扩大传感范围
3D高清地图 高清实时地图更新、地标实现亚米级精度
精确定位 GNSS定位、航迹推测、视觉惯性测距
雷达 恶劣天气条件、 远距离、弱光情况
摄像头 解读对象/信号、 成本可控的宽视野(FOV)方案
激光雷达 距离感知、中距
超声波 低成本、近距
提供高水平预测和自动化

## Slide 11: 目录
C-V2X 技术特点
C-V2X 技术现状及趋势
V2X SOTIF 相关用例及思考

## Slide 12: C-V2X技术需要持续演进
向5G演进，同时支持后向兼容
基本安全特性
802.11p或C-V2X R14
增强的安全特性
C-V2X R14
前沿安全特性
C-V2X R15+
更佳链路预算支持
更长通信距离和更高可靠性
为V2X基本服务建立基础
更高吞吐量
更高可靠性
宽带覆盖和定位
更低时延
详细的频谱规划以支持变革

## Slide 13: 充分利用ITS 5.9 GHz 带宽实现5G V2X移动车联服务
满足现有基本安全服务需求，也支持未来高级用例
10MHz分频段满足现有基本安全服务需求
（使用 802.11p 或 C-V2X）
除基本安全需求以外，70MHz带宽也能支持更高级别安全服务。（例如传感器共享高频带宽，以及宽带测距定位。）
5.9 GHz带宽应用试例
C-V2X 移动车联技术Rel-15+版可在Rel-14版相同频谱上运行
高级安全/ 5G V2X服务
(C-V2X Release 14或15+版本)
10MHz
70MHz
70 MHz
10 MHz
基本安全
服务需求

## Slide 14: C-V2X移动车联技术向5G自动驾驶演进
1. 应用PHY/MAC 通信技术; R16通信技术仍处于开发中。
D2D车与车 对点通讯
R12/13通信技术
网络独立性 | 无 | 有 | 有
通信方式1 | 只广播 | 只广播 | 广播+单播/多播
支持高速通信 | 无 | 有 | 有
支持高密度通信 | 无 | 有 | 有
通信通量 |  | 增强的安全应用性能，通量高 | 超高通量
延迟 |  | 增强的安全应用性能，延迟低 | 超低延迟
可靠性 |  | 增强的安全应用性能，可靠性高 | 超高可靠性
定位技术 | 无 | 共享定位信息 | 宽带测距及定位
自动驾驶
支持C-V2X R16 5G NR (Ph. III)通信技术
(高级安全应用技术)
安全性增强
C-V2X R14 (Ph. I) C-V2X R15 (Ph. II)通信技术
为简单D2D对点通讯
建立硬件基础
为保证C-V2X安全性
通信范围更大、可靠性更高
为满足自动驾驶
可靠性极强，延迟更低，通信通量更高
Notes: 1. C-V2X Release 16 is still being worked on by 3GPP

## Slide 15: 对比：用例和性能
用例 | 802.11p | C-V2X Rel-14/15 | C-V2X Rel-16(设计预期)
目标用例 | 只有初始安全 | 初始安全及增强安全 | 高级用例，协助自动驾驶，包括测距辅助定位，高通量传感器共享，和本地3D高清地图更新。
性能 |  |  | 
高密度使用支持 | 高密度使用下会丢包 | 高密度使用下可保证不丢包 | 高密度使用下可保证不丢包
高移动性使用支持 | Up to relative speeds of 500 km/hr with advanced receiver implementation | Up to relative speed of 500 km/hr as a minimum requirement. | Up to relative speed of 500 km/hr as a minimum requirement
传输范围（90%错误率，280千米/时相对速度下） | 最高 ~225米 | -直接通信模式下超过450米 -通过移动数据基础设施可达非常远 | -直接通信模式下超过450米 -通过移动数据基础设施可达非常远
周期性交通典型传输频率 | 每100毫秒一次 (也可每50毫秒一次) | 每100毫秒一次 (也可每20毫秒一次) | 支持数毫秒 周期性数据包传输

## Slide 16: 5G V2X车联为互联汽车带来新的功能
同时也保有向后兼容性
高通量
传感器共享
本地高清地图/
鸟瞰模式
高通量和低延迟特性保障原始或处理后的数据高效交换
高通量特性保障构建基于摄像头和传感器数据的本地动态地图，并在街道交叉路口分发
宽带
测距和定位
宽带运营商技术支持，获取准确定位和测距，来保障车辆协作与自动驾驶场景
行车意图/ 轨迹共享
高通量和低延迟特性保障计划行驶轨迹快速共享
宽带运营商支持 | 高通信通量 | 极低延迟 | 极高可靠性 | 极强安全性

## Slide 17: 目录
C-V2X 技术特点
C-V2X 技术现状及趋势
V2X SOTIF 相关用例及思考

## Slide 18: ISO/DIS 21448
V2X SOTIF implementation
V2X SOTIF concerns mainly relate to the V2X message being incorrect due to a V2X limitation
        Inaccurate
        Out of date
Issues can be detected via comparisons between the V2X message and the ego‑vehicle perception to judge the freshness and accuracy of the V2X message.
The system specification requirements for different types of V2X messages to meet tolerances specified by safety analysis of the function/system.
      Latency
      Reliability
      Update frequency

## Slide 19: ISO/DIS 21448
V2X 通信规范及设计 – 主题示例
V2X系统要求
      Latency requirement
      Reliability requirement
      Interoperability requirement
    V2X数据要求
      Accuracy requirements of the object or event included in the V2X message (location, time)
      Integrity requirements of the object or event included in the V2X message
      Precision requirement
      Resolution requirement
      Traceability requirement
      Conformance requirement
    V2X 消息的车辆级功能应用
    已知的V2X局限性

## Slide 20: C-V2X移动车联对自动驾驶安全至关重要
在充满变数挑战的实景情况下，也要准确传达意图信息和传感器数据
非视线传感
具有360°非视线传感感知，
在夜晚和恶劣天气条件下也能正常工作。
传达意图
共享行车意图、传感器数据和路径规划信息，以增加更高层级上的可预测性
环境感知
提供更广的电子视野，
支持软安全警报和分级警示
拥堵警示/车流波减速
突然变道
道路险情
交叉路口盲区/ 行道弱势人群警报
前方路况通行缓慢

## Slide 21: I2V 用例
车内标牌：速度限制
车内标牌：前方学校提醒
车内标牌：全路段禁停预警
车内标牌：前方急转弯预警

## Slide 22: I2V 用例
车内标牌：禁止鸣笛预警
红绿灯信息推送/绿波通行
车内标牌：前方加油站提醒
弱势交通参与者提醒

## Slide 23: I2V 用例
前方桥梁提醒
前方红绿灯信息
十字路口- 广播周围信息
乘客人数及到达时间

## Slide 24: V2V 用例
前向碰撞提醒
故障车辆提醒
盲区预警
左转辅助

## Slide 25: V2X一期应用
1. T/CSAE 53－2020
2.按照安全、效率、信息服务三大类的17个典型应用作为一期应用
3.根据应用对通信频率和时延的不同需求将17个一期应用分为两大类：
高时延（＞100 ms）、低频率（＜10 Hz）的应用，可通过4G蜂窝通信技术实现；
低时延（≤100 ms）、高频率（≥10 Hz）的应用，需要LTE-V2X、DSRC或5G通信技术的支持才能实现

## Slide 26: V2X一期应用列表
序号 | 类别 | 主要通信方式 | 应用名称 | 主车车速范围（Km/h) | 通信距离 （≥m） | 数据更新频率（Hz） | 系统延迟（≤ms） | 定位精度（≤m）
1 | 安全 | V2V | 前向碰撞预警 (FCW) | 0~130 | 300 | 10 | 100 | 1.5
2 |  | V2V/V2I | 交叉路口碰撞预警(ICW) | 0~70 | 150 | 10 | 100 | 1.5
3 |  | V2V/V2I | 左转辅助(LTA) | 0~70 | 150 | 10 | 100 | 1.5
4 |  | V2V | 盲区预警/变道预警(BSW/LCW) | 0~130 | 150 | 10 | 100 | 1.5
5 |  | V2V | 逆向超车预警(DNPW) | 0~70 | 300 | 10 | 100 | 1.5
6 |  | V2V-Event | 紧急制动预警(EBW) | 0~130 | 150 | 10 | 100 | 1.5
7 |  | V2V-Event | 异常车辆提醒(AVW) | 0~130 | 150 | 10 | 100 | 1.5
8 |  | V2V-Event | 车辆失控预警(CLW) | 0~130 | 300 | 10 | 100 | 1.5
9 |  | V2I | 道路危险状况提示(HLW) | 0~130 | 300 | 5 | 100 | 1.5
10 |  | V2I | 限速预警(SLW) | 0~130 | 300 | 1 | 100 | 1.5
11 |  | V2I | 闯红灯预警(RLVW) | 0~70 | 150 | 5 | 100 | 1.5
12 |  | V2P/V2I | 弱势交通参与者碰撞预警(VRUCW) | 0~70 | 150 | 5 | 100 | 1.5
13 | 效率 | V2I | 绿波车速引导(GLOSA) | 0~70 | 150 | 1(道路)/5(信号灯) | 200 | 1.5
14 |  | V2I | 车内标牌(IVS) | 0~70 | 150 | 1(道路数据与交通标牌信息) | 500 | 1.5
15 |  | V2I | 前方拥堵提醒（TJW） | 0~130 | 150 | 1 | 500 | 5
16 |  | V2V | 紧急车辆提醒(EVW) | 0~130 | 300 | 5 | 100 | 1.5
17 | 信息服务 | V2I | 汽车近场支付(VNFP) | 0~130 | 150 | 1 | 500 | N/A

## Slide 27: V2X对于安全用例提供更好的支持
禁止超车告警(DNPW) 弯道盲区/局部危险告警 道路施工改道告警
十字路口盲区辅助通过 十字路口行人警告 左转弯辅助驾驶(LTA）
通过扩展电子视野，提供更多可靠性和更好的非视距下的性能
0mph

## Slide 28: Component level analysis
Category | Performance limitation |  | SOTIF measure |  |  | Verification criteria | 
 | Qualitative description | Quantitative description | Category | Subcategory | Concrete description | Quantitative description | Quantitative description
V2X | Out of coverage of roadside infrastructure (not applicable for EBW) |  |  |  |  |  | 
 | Interference from other devices or surrounding infrastructure | Signal lost or quality degrade due to interference from surrounding devices or infrastructure: - SNR < X dB - PRR < X% | Functional restrictions | Restriction of the intended functionality for specific use cases; | Limitation of the ODD (Operational DesignDomain) including environmental, |  | 
 |  |  | Handing over authority | Modifying the user notification and DDT (Dynamic Driving Task) fallback strategy; | Hand over authority to driver if SNR is below X dB for X ms or PRR is below X% for X ms |  | 
 |  |  | System modification | Increased sensor performance and/or accuracy by improved sensor technology; | TBD |  | 
 | Data elements of object or event lost in message | Information lost during transmission: - PRR < X% | Functional restrictions | Restriction of the intended functionality for specific use cases; | Limitation of the ODD (Operational DesignDomain) including environmental, |  | 
 |  |  | System modification | Increased sensor performance and/or accuracy by improved sensor technology; | TBD |  | 
 |  |  | Handing over authority | Modifying the user notification and DDT (Dynamic Driving Task) fallback strategy; | Hand over authority to driver if PRR is below X% for X ms |  | 
 | High tolerance range that causing incorrect estimation of position for front vehicle or vehicle in adjacent lane | Positioning accuracy beyond tolerance range - Longitude range - 1.5m (all) & TTC (vehicle control related); - Lateral range - 1.5m (all) | Functional restrictions | Restriction of the intended functionality for specific use cases; | Limitation of the ODD (Operational DesignDomain) including environmental, |  | 
 |  |  | System modification | Increased sensor performance and/or accuracy by improved sensor technology; | TBD |  | 
 |  |  | Addressing misuse | Customer education(information and training) | User manual, training courses, marketing, sales presentation. | Conduct after-training survey to investigate the effectiveness of the training. | 
 | Long period of sending message | Time interval longer than threshold that lead to collision - Latency: 100 ~ 150ms for some application, may need to be less than 40ms in other applications | System modification | Increased sensor performance and/or accuracy by improved sensor technology; | Change to new and improved sensor that addresses known limitations. |  | 
 |  |  | Addressing misuse | Customer education(information and training) | User manual, training courses, marketing, sales presentation. | Conduct after-training survey to investigate the effectiveness of the training. | 
 |  |  | Functional restrictions | Restriction of the intended functionality for specific use cases; | Limitation of the ODD (Operational DesignDomain) including environmental, |  | 

## Slide 29: System level analysis
Category | Performance limitation |  | SOTIF measure |  |  | Verification criteria | 
 | Qualitative description | Quantitative description | Category | Subcategory | Concrete description | Quantitative description | Quantitative description
camera | Unable to detect objects out of FOV (Field Of View). | Unable to detect objects out of FOV (Field Of View), 120 degree. | System modification | Increased sensor performance and/or accuracy by diverse sensor types; | Leverage other sensor/tecnology to complement the out of FOV situation for camera. Could consider how to combine V2X and Camera technology here. | Conduct simulation and vehicle testing to verify if the other sensor/tecnology do complement the out of FOV situation for camera. | 

## Slide 30: SOTIF相关思考
基于V2X安全用例筛选SOTIF相关场景
  通信距离
  数据更新频率
  系统延迟
  定位精度
从部件层面及系统融合层考虑V2X的性能局限性和相关改进措施
  非视距传感
  传达意图
  环境感知