## Slide 1: Review Comments of WAPI Management Frame Protection Draft
Speaker name
  Speaker title
  Employing entity
Location
Date
@qualcomm

## Slide 2: Review comments – 1 [Qiwei]
Chapter | Original | Revision Suggestions
4 Replace article 5.4.3.2 in GB 15629.11-2003 with the following: | When a STA sends a Deauthentication message to its associated STA | When a STA sends a Deauthentication message to its associated AP [Typo?]
27 The content of 11.4.3 of item 33 in GB 15629.11-2003/XG1-2006 is replaced with the following: | 11.4.3 AP re-association | 11.4.4 AP re-association [Referring to section#11.4.4 of GB+15629.11-2003-XG1-2006.pdf]
28 The content of 11.4.4 of item 33 in GB 15629.11-2003/XG1-2006 is replaced with the following: | 11.4.4 STA disassociation | 11.4.5 STA disassociation [Referring to section#11.4.5 of GB+15629.11-2003-XG1-2006.pdf]
29 The content of 11.4.5 of item 33 in GB 15629.11-2003/XG1-2006 is replaced with the following: | 11.4.5 AP disassociation | 11.4.6 AP disassociation [Referring to section#11.4.6 of GB+15629.11-2003-XG1-2006.pdf]

## Slide 3: Review comments - 2 [Jouni]
Chapter | Original | Revision Suggestions
21 The following content is added to 8.1.2.2 of item 26 in GB 15629.11-2003/XG1-2006: | The group addressed Robust Management frame case may or may not be quite different, though, since this is documented to be using encrypted frames with CBC-MAC mode with WPI-SM4 | 
17 Add article 7.3.2.9 in GB 15629.11-2003: | The type field is 2 (decimal) | Expected the type field to be one octet in size. The Element ID 2 in IEEE 802.11 is marked as being "Reserved". It would be safer to use a vendor specific element or request a unique element identifier ID value from IEEE 802.11 to avoid conflicts
22 The following content is added to the last paragraph of 8.2.3 of item 26 in GB15629.11-2003/XG1-2006: | The MMIE field contains 26 octets. MMIE field: 35 octets. Where the KeyID field is set to the KeyID value of the corresponding multicast session key MSK. The MIC field is set to 0. The PN is the management data packet number corresponding to KeyID. When the CBC-MAC mode is used to calculate the integrity verification code MIC in WPI-SM4……Using the multicast integrity verification key and the management data packet number PN, the check algorithm working in CBC-MAC mode calculates the multicast management protocol data, and the integrity verification code MIC is obtained. | The MMIE should be consistently documented as having the size of 26 octets. The description of CBC-MAC mode in this subclause seems implying only integrity protected, while the other parts of the document were clearly using "encrypted" in the context of multicast Robust Management frames.

## Slide 4: Review comments - 3 [Rohan]
Chapter | Original | Revision Suggestions
16 Substitute article 7.3.2.8 in item 25 in GB 15629.11-2003/XG1-2006 to: | The element ID shall be 68. | Element ID 68 of WAPI is conflict with BSS AC Access Delay defined in IEEE 802.11.
17 Add article 7.3.2.9 in GB 15629.11-2003: | IPN field, an integral containing six octets, identifies the multicast management packet number (PN in WPI multicast management group) that has been encrypted and sent with the currently notified key. | WAPI PN is generally 16 Bytes (section 7.3.2.8.1) [Referring to section#8.1.4.4.1 of GB+15629.11-2003-XG1-2006.pdf]
17 Add article 7.3.2.9 in GB 15629.11-2003: | The subsequent data frame number received by the STA shall be greater than the value of this field; otherwise, it shall be discarded to detect and resist replay attacks on protected multicast robustness management frames. | The IPN mentioned in the same section 7.3.2.8.1 states that the subsequent data frame PN should be greater than IPN in MMIE . Please kindly help clarify this , the PN is maintained ideally per key & Tid , so for IGTK we have one PN, hence why the PN in multicast mgmt. frame should dictate the data frame PN as stated below in the document ?

## Slide 5: Review comments – 4 [Kun]
Chapter | Original | Revision Suggestions
21 The following content is added to 8.1.2.2 of item 26 in GB 15629.11-2003/XG1-2006: | Whengb15629dot11wapiProtectedManagementFramesEnabled of the STA is set to False, the STA shall send and receive unprotected unicast robustness management frames with any associated STAs and discards all received protected unicast robustness management frames. | Whengb15629dot11wapiProtectedManagementFramesEnabled of the STA is set to False, the STA shall send and receive unprotected unicast robustness management frames with any associated APs and discards all received protected unicast robustness management frames. [Typo?]